## Slide 1: Introduction to FPGAs Lecture 1: FPGAs, Logic Gates, Programming an FPGA
Adam Duncan Ph.D.

## Slide 2: Class Introduction
About Me: Electrical/Computer Engineer at NSWC Crane
Class Goals: 1) Learn about FPGAs. 2) Program FPGAs to do fun things.
Class SW Materials: https://github.com/adamdunc/whs

## Slide 3: Field-Programmable Gate Arrays (FPGAs) are “Programmable Hardware” devices
FPGA
~1 inch2 with ~10 billion transistors
Not as Fast (~500MHz)
Hardware can be programmed to do anything
CPU
~1 inch2 with ~10 billion transistors
Fast (~3GHz)
Hardware does one thing really well (execute code)

## Slide 4: FPGA hardware behavior configured by “Bitstream” file
FPGA
CPU
CPU is always CPU Datapath
CPU
Bitstream
FPGA is now CPU Datapath
FPGA is now Neural Network Datapath
Neutral Network
Bitstream
FPGA is now customized sensor driver/sampler
Custom
Sensor
Bitstream

## Slide 5: FPGA benefits
HW ultimately drives performance (SW optimizations limited by HW)
Parallelization (i.e. 35 parallel ALUs executing at same time)
Unique needs (read non-standard sensors at deterministic time intervals)
Consolidates PCB circuitry (CPU + sensor logic + display driving)
Prototype Custom Integrated Circuits (wafers >$10M)
Update hardware in field (security updates, new features, bug fixes)
Replace obsolete hardware (configure FPGA to “emulate” obsolete component”

## Slide 6: FPGAs in the Wild
Ease of use:
New HW designs in ~1 day
Design portability
Cost:
$1 for low-cost FPGAs
$100K for rugged/large FPGAs
Products with FPGAs:
Consumer electronics
DoD Programs
Automotive
Networking equipment
Test/Measurement equipment

## Slide 7: FPGA Demo: Yoshi’s Nightmare on our class FPGA
We can configure the FPGA to emulate video game system driving a display
https://github.com/jconenna/Yoshis-Nightmare
NES Classic Circuit Board
FPGA replacing CPU/GPU, RAM, Flash

## Slide 8: Meet Our FPGA: Xilinx Artix7 on a BASYS3 PCB
Xilinx Artix7 FPGA with 35K gates
USB/UART
VGA
Pushbuttons
LEDs
Slide Switches
7-segment LEDs
https://reference.digilentinc.com/basys3/refmanual

## Slide 9: This week we design/simulate/program an FPGA!
Monday:
  (morning) Project 0: Program your FPGA with a pre-made file to play “Yoshi’s Nightmare”
  (morning) Project 1: Build a half adder circuit with logic gates on a breadboard
  (afternoon) Project 2: Design/Program your FPGA to behave like a half adder
  (afternoon) Project 3: Simulate your half adder project
Tuesday:
  Project 4: Design/Simulate/Program your FPGA to behave as a calculator
  Project 5: Design/(Simulate)/Program your FPGA to behave as a UART to communicate with your computer.
Wednesday:
  Project 6.0: Design/(Simulate)/Program your FPGA to play basic Pong
  Project 6.1: Add Pong features: scoring, keyboard control, sounds, etc
Thursday:
  Project 6.1 continued: Add more Pong features: scoring, keyboard control, sounds, etc
Friday
  Project Brief Outs

## Slide 10: Project 0: Program FPGA to Play Yoshi’s Nightmare in 7 Easy Steps!
Open Vivado on laptop
Connect BASYS3 to laptop with micro-usb cable
Connect BASYS3 to monitor with VGA cable
Open Hardware Manager in Vivado
  Click “autoconnect”
  Select Program File “nightmare.bit”
  Click “Program”
Use center pushbutton to start game
Use left/right/up pushbutton to move Yoshi
Try to score more than 620 points
Project 0 Goals:
Run Vivado FPGA EDA software
Program FPGA to do something

## Slide 11: FPGA hardware behavior controlled by “logic gates” that implement Boolean equations
https://en.wikipedia.org/wiki/Logic_gate
FPGAs contain up to 20 million logic gates!
“AND” logic gate

## Slide 12: Project 1: Add two binary numbers (half adder) with logic gates on a breadboard
Half Adder
(Decimal)
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 2
Half Adder
(Binary)
0 + 0 = 00
0 + 1 = 01
1 + 0 = 01
1 + 1 = 10
Decimal to binary conversion
Project 1 Goals:
Learn about logic gates
Build a physical circuit with logic gates

## Slide 13: We can build a half-adder circuit with two logic gates
Note that our FPGA (Artix7 A35T has 35000 gates inside it!)
Half Adder “Truth Table”
Half Adder “Circuit” with XOR and AND “Gates”

## Slide 14: Let’s build our 5V half-adder with logic gates on a breadboard
Half Adder “Truth Table”
Half Adder “Circuit” with XOR and AND “Gates”
GND
GND
GND
A = RED
(0 = unpressed, 1 = pressed)
B = Blue
(0 = unpressed, 1 = pressed)
+5V
330Ω
GND
+5V
330Ω
S = Yellow
(0 = unlit, 1 = lit)
C = Green
(0 = unlit, 1 = lit)
5V
(col
with +)
GND (col with “-”)

## Slide 15: Datasheets show pin connections for the “gates” in our half adder
AND Gate
Datasheet
XOR Gate Datasheet

## Slide 16: Project 1: Assemble breadboard
1) Place components on breadboard
2) Add blue wires, LEDs, and 330 ohm resistors
SN74LS08
“AND Gate”
SN74AHCT86
“XOR Gate”
Power
Supply
Pushbuttons
5V “+” column
0V “-”
column
3) Add red wires to blue button and 330Ω resistor
LEDs with “long side” in 5V column
resistors
4) Add black wire to “0V” and white wire to “5V”

## Slide 17: Project 1: Assemble breadboard
5) Connect blue, red, white, black wires to XOR gate. Connect 9V battery to power supply

## Slide 18: Let’s test our half-adder breadboard solution
Half Adder “Truth Table”
Inputs: A=0,B=0 outputs: C=0,S=0
Inputs: A=1,B=0 outputs: C=0,S=1
Inputs: A=0,B=1 outputs: C=0,S=1
Inputs: A=1,B=1 outputs: C=1,S=0

## Slide 19: Introduction to FPGAs Lecture 2: Design/Simulate FPGA Design with Vivado
Adam Duncan

## Slide 20: Vivado and FPGA Design 101
Xilinx Vivado a software program used to design, program, simulate your FPGA.
We write a code in a hardware description language (HDL) like Verilog to specify the intended hardware behavior of the FPGA.
Vivado compiles the Verilog and automatically places logic gates inside the FPGA to realize the intended FPGA functionality.
Vivado produces a bitstream file that is loaded into the physical FPGA to configure the FPGA behavior.

## Slide 21: Verilog 101: Verilog, module, assign
  A Verilog module is a hierarchal block in Verilog within input/output ports
  An assign statement performs assignments and arithmetic operations on ports and wires within a module.
  module top(
  output LED
  );
  assign LED = 1;
  endmodule

## Slide 22: Vivado 101: XDC files
  Xilinx Vivado a software program that turns Verilog into a bitstream file that can configures the hardware behavior of an FPGA.
  Xilinx design constraints (XDC) files map FPGA physical pins to Verilog top-level module ports.
  set_property PACKAGE_PIN U16 [get_ports {LED}]
  set_property IOSTANDARD LVCMOS33 [get_ports {LED}]

## Slide 23: Project 2: Create half adder Vivado project from scratch
0) Open Vivado and create new project with default options
1) New Project
  Click “Do not specify sources at this time”
2) Select Part “xc7a35ticpg236-1L”
Follow steps outlined in below link if needed: https://users.wpi.edu/~rjduck/Basys3%20Vivado%20Decoder%20Tutorial.pdf
Project 2 Goals:
Use Vivado to create an FPGA design
Use Vivado to program your FPGA design

## Slide 24: Project 2: Create half adder Vivado project from scratch
3) create design file “top.v”
  module top(
  input A, // input port
  input B, // input port
  output SUM, // output port
  output CARRY // output port
  );
  assign SUM = A ^ B; // bitwise xor
  assign CARRY = A & B; // bitwise and
  endmodule
Follow steps outlined in below link as needed https://users.wpi.edu/~rjduck/Basys3%20Vivado%20Decoder%20Tutorial.pdf
4) create constraints file “top.xdc”
  set_property PACKAGE_PIN V17 [get_ports A] set_property IOSTANDARD LVCMOS33 [get_ports A] set_property PACKAGE_PIN V16 [get_ports B] set_property IOSTANDARD LVCMOS33 [get_ports B] set_property PACKAGE_PIN U16 [get_ports SUM] set_property IOSTANDARD LVCMOS33 [get_ports SUM] set_property PACKAGE_PIN E19 [get_ports CARRY] set_property IOSTANDARD LVCMOS33 [get_ports CARRY]

## Slide 25: Program half adder bitstream FPGA on BASYS3
Open “Hardware Manager” in Vivado
Click “Program Device”
Select “top.bit”from “~/WHS/Projects/student_p1.runs/impl_1“ or equivalent directory
After FPGA is programmed toggle SW0,SW1
  You should see LED0,LED1 toggle
Toggle SW0,SW1 to activate LED0,LED1

## Slide 26: Half adder Vivado Project View

## Slide 27: Open Synthesized Design to see “logic gate” usage
Logic Gates

## Slide 28: FPGA 101: Simulations
  FPGA simulations allow you to control and observe the behavior of your Verilog code.
  Simulations are useful for assessing performance and debugging.
  Simulations allow you to control/observe signals internal to the circuit running on the FPGA.

## Slide 29: Verilog 101: Testbenches
  A Verilog testbench is an HDL file that instantiates a Verilog module to simulate its behavior.
  Testbench uses Verilog code to stimulate the module being tested.

## Slide 30: Project 3: Simulate your half adder
0) Open your half adder Vivado project
Create simulation source “tb_top.v”
Add code as directed in the Project 3 README
Follow steps outlined in below link if needed: https://users.wpi.edu/~rjduck/Basys3%20Vivado%20Decoder%20Tutorial.pdf
Project 3 Goals:
Use Vivado to simulate an FPGA design

## Slide 31: Project 3: Create tb_top.v testbench file and simulate

## Slide 32: Run Vivado “Simulate”

## Slide 33: Project 4: Design/Simulate/Program your FPGA to be a calculator
Add code as directed in the Project 4 README
Follow steps outlined in below link if needed: https://users.wpi.edu/~rjduck/Basys3%20Vivado%20Decoder%20Tutorial.pdf
Project 3 Goals:
Learn useful Verilog syntax and features
Utilize 7-segment LEDs
See github/adamdunc/whs for README

## Slide 34: Project 4 Step 1: Design/Simulate Calculator

## Slide 35: Project 4 Step 2: Note increased logic gate usage

## Slide 36: Verilog 101: always, reg
  An always block executes any time the contents within its parenthesis toggle.
  A reg is a register
  module top(
  input [7:0] A, input [7:0] B, output reg [15:0] Z
  );
  always @ (*)
  begin
  if (btnU == 1)
  Z = A + B;
  else if (btnL == 1)
  Z = A / B;
  end
  endmodule

## Slide 37: Project 4 Step 3: Modify calculator to include always block to select more operands

## Slide 38: Introduction to FPGAs Lecture 3: Sequential Logic, UART
Adam Duncan

## Slide 39: Sequential logic 101: Clocks and Memory
https://www.elprocus.com/tutorial-on-sequential-logic-circuits/
Combinational: output toggles after input (No memory)
Sequential: output toggles with input, previous state, and clock signal edge (Memory)

## Slide 40: UART 101: Parallel versus Serial
https://learn.sparkfun.com/tutorials/serial-communication/all

## Slide 41: UART 101: Hardware blocks to convert between serial and parallel data
https://learn.sparkfun.com/tutorials/serial-communication/all
8 bit parallel
1 bit serial
1 bit serial

## Slide 42: Project 5: Design/(simulate)/Program FPGA to function as UART to communicate with PC
https://github.com/alexforencich/verilog-uart/
2) ASCII “1” sent serially over USB to FPGA
1) User presses “1” on PC keyboard
3) FPGA receives ASCII “1”, and sends it back to PC
4) ASCII “1” sent serially over USB back to PC
Project 5 Goals:
Communicate with FPGA from PC
Experience sequential logic and UARTs
See github/adamdunc/whs for README

## Slide 43: Project 5 Step 1: Instantiate “uart_rx” and “uart_tx” modules
https://github.com/alexforencich/verilog-uart/
See github/adamdunc/whs for README

## Slide 44: Project 5 Step2: Connect UART RX and UART TX modules together with axis_tdata, axis_tvalid, axis_tready

## Slide 45: Project 5 step 3: Add logic inside FPGA to “modify” the ASCII values inside the FPGA

## Slide 46: Project 6: Generate Basic “Pong” Game
Open Project 6 Vivado Pong project
  Add Verilog to drive VGA output from FPGA
  (See README for specific files and lines to add)
  Generate bitstream
  Program bitstream on FPGA
Connect VGA output from FPGA board to monitor
Use “left” and “right” keys to control paddle
We will use this as the base for our final project!
https://www.fpga4fun.com/PongGame.html
Project 6 Goals:
Build simple Pong game on FPGA
Customize Pong with your group!
See github/adamdunc/whs for README